Changing an Empty Dewar:

- On the dewar that is empty:

  - Shut the needle valve on the regulator.

  - Shut the valve the dewar “gas” valve.

- Remove the regulator from the dewar

- Roll the empty dewar in the hall

- Shut the needle valve of the other dewar

- On the new full dewar:

  - Attach the regulator to the new dewar.

  - Open the dewar “gas” valve

  - Close the three-way valve on the line connecting the two dewars

  - Open the needle valve on the regulator

  - Open the three-way valve to vent and flush the line for a 10 seconds.

  - Rotate the three-way valve 180 degrees to allow the new dewar to supply gas to the system

6.	Open the needle valve on the regulator on the other dewar.

7.	Call physical plant (x4891) and order a new dewar (the instructions are on the wall next to the phone).

IF THESE INSTRUCTIONS CONFUSE YOU, DO NOT ATTEMPT TO CHANGE THE DEWAR.  CONTACT LAUREN OR BRUCE FOR HELP.